## Slide 1
ZRapid iAMC150 (Additive Manufacturing Ceramics)
Specifications:
Building VAT | 
Volume | Approx. 2.3L @100mm(Z)
XY platform | 150mm(X)×150mm(Y)
Z axis | 100mm(standard) / ≤150mm(custom)
Ceramic paste | Cera Al₂O₃(alumina) / Cera ZrO₂(zirconia) etc.
SOFTWARE | 
Data interface | STL file, CLI file
Build software | ZERO 5.0 build software
Preparation software | 3dMagic
CAD interface | 3D design software, STL file format
INSTALLATION CONDITION | 
Power | 200-240VAC 50/60Hz, single phase, 5/10Amps
Ambient temperature | 20-26℃
Relative humidity | Less than 30%, non-condensing
Size | 1.45m(W)×0.93m(D)×1.90m(H) (Operating computer is not included)
Weight | Approx. 800kg
LASER SYSTEM Type | Diode-pumped solid-state laser Nd:YVO₄
Wavelength | 354.7nm
Power | 3000mW (Build:300~1500mW)
Cooling mode | Circulating water cooling
RECOATING SYSTEM | 
Process | Intelligent Linkage Double Cylinder Coating System
Normal build style | 0.05mm
Quick build style | 0.05~ 0.1mm
Precision build style | 0.02~0.05mm
OPTICAL & SCANNING | 
Beam (diameter@1/e²) | 0.06-0.12mm
Focus style | High speed galvanometer scanner
Part drawing speed | 1.0~4.0m/s (Recommended)
Beam jump speed | 10.0m/s (Recommended)
Reference building speed | 2~5cm³/h
ELEVATOR | 
Elevator motor | High accuracy servo motor
Position repeatability | ±0.01mm
Platform | Marble benchmark platform